# Pipeline Pigging Specialties Ltd.

603 – 21 Ave. 						                   		                PH: (780) 955-7776

## NISKU, AB. T9E 7X9     					      		             FAX: (780) 955-2527

E-Mail: info@pipelinepigging.ca                    		                             www.pipelinepigging.ca

# OPEN CELL POLYURETHANE FOAM

- Light Density (2.5lb/ft3)

  - Medium Density (3-5lb/ft3)

    - Hard Density (8-10 lb/ft3)

93A Durometer Polyurethane Coating

(Colored to Specific Densities)

Sizes Available = 0.3” to 48” O.D.

Available in Sphere Design = .075” to 12.25”

Hand Launchable & Compressible

RBS (RED BARE SQUEEGEE)

- Regular wiping and dewatering of pipelines

- Line proving

- Gauging pig to determine pipeline I.D.

- Removal of thick, soft internal deposits

- Condensate and liquid removal from wet gas systems

- Product removal

- Pigging multi-diameter pipelines

- Used as sealing pig

- Available in double dish (bi-directional) applications

- Handling ropes optional

- Transmitter cavities available for electronic tracking equipment

RCC (RED CRISS-CROSS)   Most Common in 5lb. Density

- Regular wiping and dewatering of pipelines

- Hydro-testing, Air-testing & mud plugging

- Removal of thick, soft internal deposits

- Condensate and liquid removal from wet gas lines

- Paraffin removal from crude oil pipelines

- Non-abrasive scraping

- Urethane coating enhances cleaning and wear resistance

- Used when there is danger of damaging the interior of the pipe

- Available in double dish (bi-directional) & Bullet Nose

- Handling ropes available

- Transmitter cavities for electronic tracking equipment

- Long wear resistant up to 100 kilometers

RCCWB (Red Criss-Cross Wire Brush) Most Common in 5lb. Density

- Regular scraping of pipelines

- Recommended for most corroding pipelines

- Removal of welding debris or other foreign materials after new construction

- Used to remove hard scale, paraffin’s and heavy material

- Available in a turning pattern for more aggressive cleaning

- Available in double dish (bi-directional) applications

- Handling rope or cables optional

- Transmitter cavities for electronic tracking equipment optional